## Slide 1: Design of Digital Circuits Lecture 19a: VLIW
Prof. Onur Mutlu
ETH Zurich
Spring 2019
3 May 2019

## Slide 2: Approaches to (Instruction-Level) Concurrency
Pipelining
Out-of-order execution
Dataflow (at the ISA level)
Superscalar Execution
VLIW
Fine-Grained Multithreading
Systolic Arrays
Decoupled Access Execute
SIMD Processing (Vector and array processors, GPUs)

## Slide 3: VLIW

## Slide 4: VLIW Concept
Superscalar
  Hardware fetches multiple instructions and checks dependencies between them
VLIW (Very Long Instruction Word)
  Software (compiler) packs independent instructions in a larger “instruction bundle” to be fetched and executed concurrently
  Hardware fetches and executes the instructions in the bundle concurrently
No need for hardware dependency checking between concurrently-fetched instructions in the VLIW model

## Slide 5: VLIW Concept
Fisher, “Very Long Instruction Word architectures and the ELI-512,” ISCA 1983.
  ELI: Enormously longword instructions (512 bits)

## Slide 6: VLIW (Very Long Instruction Word)
A very long instruction word consists of multiple independent instructions packed together by the compiler
  Packed instructions can be logically unrelated (contrast with SIMD/vector processors, which we will see soon)
Idea: Compiler finds independent instructions and statically schedules (i.e. packs/bundles) them into a single VLIW instruction
Traditional Characteristics
  Multiple functional units
  All instructions in a bundle are executed in lock step
  Instructions in a bundle statically aligned to be directly fed into the functional units

## Slide 7: VLIW Performance Example (2-wide bundles)
lw $t0, 40($s0)
add $t1, $s1, $s2
sub $t2, $s1, $s3 and $t3, $s3, $s4 or $t4, $s1, $s5
sw $s5, 80($s0)
Ideal IPC = 2
Actual IPC = 2 (6 instructions issued in 3 cycles)

## Slide 8: VLIW Lock-Step Execution
Lock-step (all or none) execution: If any operation in a VLIW instruction stalls, all instructions stall
In a truly VLIW machine, the compiler handles all dependency-related stalls, hardware does not perform dependency checking
  What about variable latency operations?

## Slide 9: VLIW Philosophy
Philosophy similar to RISC (simple instructions and hardware)
  Except multiple instructions in parallel
RISC (John Cocke, 1970s, IBM 801 minicomputer)
  Compiler does the hard work to translate high-level language code to simple instructions (John Cocke: control signals)
    And, to reorder simple instructions for high performance
  Hardware does little translation/decoding  very simple
VLIW (Josh Fisher, ISCA 1983)
  Compiler does the hard work to find instruction level parallelism
  Hardware stays as simple and streamlined as possible
    Executes each instruction in a bundle in lock step
    Simple  higher frequency, easier to design

## Slide 10: Commercial VLIW Machines
Multiflow TRACE, Josh Fisher (7-wide, 28-wide)
Cydrome Cydra 5, Bob Rau
Transmeta Crusoe: x86 binary-translated into internal VLIW
TI C6000, Trimedia, STMicro (DSP & embedded processors)
  Most successful commercially
Intel IA-64
  Not fully VLIW, but based on VLIW principles
  EPIC (Explicitly Parallel Instruction Computing)
  Instruction bundles can have dependent instructions
  A few bits in the instruction format specify explicitly which instructions in the bundle are dependent on which other ones

## Slide 11: VLIW Tradeoffs
Advantages
  + No need for dynamic scheduling hardware  simple hardware
  + No need for dependency checking within a VLIW instruction  simple hardware for multiple instruction issue + no renaming
  + No need for instruction alignment/distribution after fetch to different functional units  simple hardware
Disadvantages
  -- Compiler needs to find N independent operations per cycle
  -- If it cannot, inserts NOPs in a VLIW instruction
  -- Parallelism loss AND code size increase
  -- Recompilation required when execution width (N), instruction latencies, functional units change (Unlike superscalar processing)
  -- Lockstep execution causes independent operations to stall
  -- No instruction can progress until the longest-latency instruction completes

## Slide 12: VLIW Summary
VLIW simplifies hardware, but requires complex compiler techniques
Solely-compiler approach of VLIW has several downsides that reduce performance
  -- Too many NOPs (not enough parallelism discovered)
  -- Static schedule intimately tied to microarchitecture
  -- Code optimized for one generation performs poorly for next
  -- No tolerance for variable or long-latency operations (lock step)
++ Most compiler optimizations developed for VLIW employed in optimizing compilers (for superscalar compilation)
  Enable code optimizations
++ VLIW successful when parallelism is easier to find by the compiler (traditionally embedded markets, DSPs)

## Slide 13: An Example Work: Superblock
Lecture Video on Static Instruction Scheduling
  https://www.youtube.com/watch?v=isBEVkIjgGA
Hwu et al., The superblock: An effective technique for VLIW and superscalar compilation.
The Journal of Supercomputing, 1993.

## Slide 14: Another Example Work: IMPACT
Chang et al., IMPACT: an architectural framework for multiple-instruction-issue processors. ISCA 1991.

## Slide 15: Design of Digital Circuits Lecture 19a: VLIW
Prof. Onur Mutlu
ETH Zurich
Spring 2019
3 May 2019